Jud Smith clinic 8/8/17

Jib

Carry looser halyard

Be sure to let the headstay take the load, not the jib luff

Under 10 knots, the backstay is the headstay control

It’s ok for the headstay to be a bit floppy

Ease jib until the leech telltale is flowing

Jib tack needs to be low on the deck.

Jib cut for 3.5” of sag—12 knots.  In light air, carry around 9”.  With one or two people on the rail, 5-7”

Smooth out jib scallops once the wind is 12 and up.

Main

No reason not to be above centerline unless overpowered.

Traveller up to the point where we have too much helm—power up so we can point

Carry a looser outhaul

Light air—ram can go to 5, which allows us to use the backstay more

10 knots—1.5” of prebend

Headstay

Lighter air, can ease another ¼” or so from our lightest setting

Rig

Base—Uppers 20, lowers 12 (these are different numbers than I received from him before)

Backstay:  17 knots: 5.5” down from neutral. 9 knots and under: 2.5” up from neutral.  Neutral is for around 10 knots.  Never go tighter than 5.5”.

Try putting the tension gauge on the headstay at mooring and seeing the effects of ram and backstay tension

Downwind

Put on enough frac to invert mast a few inches.  Don’t do this in heavy air.

Mark backstay for maximum out (downwind setting)

Mast forward makes the main work better—creates flow off the sail

Reaching—keep mast straight up and down.

Yard-sale leeward mark roundings—deal with backstay, etc., after you round.  We need to give this a try.  Might be a bit crazy.

Replace nylon ferruls on Loose guage with metal?