iStart Operation

Getting Ready

- Press POWER to turn on

- Press MODE and hold for 3 secs

- Current Mode setting will flash and display either:

  - P:53 = Normal Start

  - P:55 = Start after Postponement

  - Note:  both Modes are for a rolling sequence

- If the desired Mode is displayed --> Do Nothing

- If the desired Mode is NOT displayed --> push MODE 1X to toggle to other Mode

- After a few seconds the display will stop flashing and 6:00 will appear on the screen

- The iStart is now ready for the start sequence

- Note:  If you are in Mode selection mode (as described above) you can toggle multiple times between modes by pressing MODE

Normal Start (note: times relative to first Start)

- 6:00 – Press START/RESET

- 6:00 – 5 short Alert horns will sound

- iStart will signal 30, 20, 10 and 5, 4, 3, 2, 1 with beeps prior to Warning, Prep up, Prep down and Start

- After last Start – Press and Hold START/RESET for 3 secs to stop the iStart

More info on the back -->

Start after Postponement (note: times relative to first Start)

- This sequence starts with lowering of the AP flag !!!

- 6:00 – Press START/RESET and Lower the AP flag

- 6:00 – 1 long horn will sound

- iStart will signal 30, 20, 10 and 5, 4, 3, 2, 1 with beeps prior to Warning, Prep up, Prep down and Start

- After last Start – Press and hold START/RESET for 3 secs to stop the iStart

To Abort a start sequence (e.g if you need to postpone)

- Press and Hold START/RESET for 3 secs

- Press HORN as needed to signal AP or Abandonment

When you are done with the start sequence

- If you used Mode 55 after a postponement, go into Mode selection mode (as described in “Getting Ready”) and reset iStart back to Mode 53 for next user

Other Important Points

- To turn off the iStart – Press and hold POWER for 3 secs

- Unit needs to be powered ON to use MANUAL horn

- Press the HORN button to manually sound the horn for:

  - Shorten Course

  - Abandonment

  - Whenever else you might need a horn

- iStart is wired through the “Horn” breaker on the DC panel

  - If DC Power is on and you are not getting power to the iStart unit, check the breaker